Features :

- High Quality

- Very Stable

- Fully Plated

- IP 68 compliance

- Armed cable (optional)

- Private protocol (optional)

Specification :

- Model						-	DL44

- Capacity					-	30 Ton

- Rated Output				-	3000d mv/V

- Zero Balance				-	(( 1% F.S

- Creep (30min)				-	(( 0.02% F.S

- Non – Linearity				-	(( 0.02% F.S

- Hysteresis					-	(( 0.02% F.S

- Repeatability					-	(( 0.02% F.S

- Temperature Effect on Output		-	(( 0.02% F.S / 10K

- Temperature Effect on Zero		-	(( 0.02% F.S / 10K

- Operating Temperature Range		-	-30̇ͦ C~ 70ͦ C

- Compensated Temperature Range	-	-10̇ͦ C~ 60ͦ C

- Safety Overload				-	150% F.S

- Ultimate Overload				-	200% F.S

- Input Resistance				-		\

- Output Resistance				-		\

- Material					-	Alloy Steel

- Cable Length				-	16 Meter

- Insulation Resistance			-	≥5000Mῼ

- Excitation					-	5 VDC – 12 VDC

Wiring Code

Red		Input (+ Excitation)	+Ve

Black 	Input (- Excitation		-Ve

Green	Output (+ Signal)		+SE

White	Output (- Signal)		-SE

Yellow	Shield				Earth

Caution

Changing cable length will affect the above specification.

--------------------------------------------------------------------------------------------------------------

PRIME  Telelink Pvt. Ltd.

F-76(A1), Road 5C, V.K.Industrial Area,

JAIPUR - 302013 (INDIA)

Phone	     : +91-141-2338392, 2337737, Mob.:  +91 - 9414144444

Email 	     : prime44a@yahoo.com,   mail@primetelelink.com

Website     : www.primetelelink.com

# Text boxes

PRIME Digital Load cell